## Slide 1
Homework 1

## Slide 2
1. Add three 8-bit numbers
Statement: Add the contents of three memory locations 4000H, 4001H, and data in memory location 4002H.
Store result in location 4005H (low byte) and 4006H (high byte).
    Example problem
    4000H = 80H
    4001H = 7AH
    4002H = 0FH
    Result
    4005H = 09H
    4006H = 01H

## Slide 3
2. Add two 8-bit number and subtract one 8-bit number
Statement: Add the contents of three memory locations 4000H, 4001H, and subtract data in memory location 4002H.
Store result in location 4005H (low byte) and 4006H (high byte).
    Example problem
    4000H = FAH
    4001H = DAH
    4002H = 0FH
    Result
    4005H = C5H
    4006H = 01H

## Slide 4
3. Add three 16-bit number
Statement: Add the 16-bit number in memory locations 4000H and 4001H to the 16-bit number in memory locations 4002H and 4003H and 16-bit number in memory location 4004H and 4005H.
Store result in location 4008H (low byte) and 4009H (high byte).
    Example problem
    4000H = 55H
    4001H = 12H
    4002H = 33H
    4003H = 22H
    4005H = 44H
    4006H = 11H
    Result
    4008H = CCH
    4009H = 45H

## Slide 5
4. Add two 16-bit number and subtract one 16-bit number
Statement: Add the 16-bit number in memory locations 4000H and 4001H to the 16-bit number in memory locations 4002H and 4003H and subtract 16-bit number in memory location 4004H and 4005H.
Store result in location 4008H (low byte) and 4009H (high byte).
    Example problem
    4000H = 55H
    4001H = 12H
    4002H = 77H
    4003H = 55H
    4005H = ACH
    4006H = 45H
    Result
    4008H = 20H
    4009H = 22H